## Slide 1: Low-cost Appliance State Sensing for Energy Disaggregation
- Preliminary results
Notes: Low-cost Appliance State Sensing for Energy Disaggregation

## Slide 2: Outline
System design
  Hardware
  Event detection algorithm
  Network protocol
Network test
  Packet collision test
  Poisson distribution random event test
Experimental setup
Power disaggregation algorithm
  Piece-wise constant (PWC) de-noise
  Disaggregation algorithm

## Slide 3: Sensor node hardware
Low-cost design
  Components cost
    $4.0 @ 1
    $2.3 @ 1k
DC Power supply
(Voltage-drop capacitor)
MCU
(6pin AT-tiny)
200x
RFTX
L
N
1mΩ
AIN

## Slide 4: Event detection algorithm
Sample AC instantaneous current at ~1.6kHz for ~12ms, take the range (max-min, signal maybe clipped)
Take a threshold with hysteresis, get instantaneous binary state
Pass the instantaneous binary states through a de-bouncing smoother (counter), get appliance state
If state changes, initiate transmissions

## Slide 5: Network protocol
Each packet is 16-bit long
  1st byte
    6b – Device ID
    2b – Retransmission group number
  2nd byte
    4b – Sequence number
    3b – Retransmission slot number within group
    1b – Appliance state
Each packet’s air-time is 62ms (< 4 AC cycles)
5 transmissions for each event
  1st – when event happens
  2nd-5th – randomly chosen from 31 slots arranged in 4 groups (8,8,8,7 slots in each group)
  Each slot is 4 AC cycles long
  Whole 5 transmissions can take ~2.2s (128 AC cycles)
Group3
Group2
Group1
Group0
4Cycle x8
4Cycle x7
Initial TX

## Slide 6: Outline
System design
  Hardware
  Event detection algorithm
  Network protocol
Network test
  Packet collision test
  Poisson distribution random event test
Experimental setup
Power disaggregation algorithm
  Piece-wise constant (PWC) de-noise
  Disaggregation algorithm

## Slide 7: Packet collision test
2 events less than 2.2s apart are considered ‘collision’
  5 transmissions take at most 2.2s
Test setup
  3 sensor nodes
  Collided events, 2 at a time on 2 nodes, are generated by an external microcontroller (MBED)

## Slide 8: Packet collision test results
Time between collided events (s)
Rate
Packet delivery
Event delivery

## Slide 9: Poisson distribution random event test
Test setup
  6 sensor nodes
  Poisson distributed event sequence
    λ= expected # of events in 1 second
    1/λ = expected interval between events
    Events randomly assigned to 1 of the 6 nodes

## Slide 10: Poisson distribution random event test results
1/λ Expected time between events (s)
Rate
Packet delivery
Event delivery

## Slide 11: Real data statistics
Sensor ID
Rate
Overall packets
  4931/5252 (93.89%)
Overall events
  1108/1113 (99.55%)

## Slide 12: Outline
System design
  Hardware
  Event detection algorithm
  Network protocol
Network test
  Packet collision test
  Poisson distribution random event test
Experimental setup
Power disaggregation algorithm
  Piece-wise constant (PWC) de-noise
  Disaggregation algorithm

## Slide 13: Experimental setup
20 nodes deployed
  9 LCD monitors
  8 Laptops
  1 solder station
  1 workbench light
  1 water dispenser
13 nodes are instrumented with Watts up? PRO meter for ground truth
  2s interval
  Data collected with Gumstix and logged in database
Aggregated power reading from E30A panel meter
  2s interval
  Actually sum of 4 circuits

## Slide 15: Outline
System design
  Hardware
  Event detection algorithm
  Network protocol
Network test
  Packet collision test
  Poisson distribution random event test
Experimental setup
Power disaggregation algorithm
  Piece-wise constant (PWC) de-noise
  Disaggregation algorithm

## Slide 16: Piece-wise constant (PWC) de-noise
Adapted from ‘Jump penalization’ algorithm
Can detect step changes smaller than the variance
Online algorithm
  Adjustable sensitivity based on sensor events
Need comparison with total variation denoising (TVD)

## Slide 17: PWC results
timestamp
Power (kW)
100s

## Slide 18: PWC results
timestamp
Power (kW)
100s

## Slide 19: Disaggregation algorithm
All appliances are 2-state, on-or-off
Resolving overlapping events
  Based on history of the appliances’ power signature
PWC
(step detection)
Central power readings
Sensor network
Appliances events
Event-step match
Detect overlapping events
Disaggregated power log
Resolve overlapping events
Steps
Received events
Events with power step
Single event
Overlapping events

## Slide 20
Disagg- output
Ground truth
Selected disaggregation result (without overlapping events)

## Slide 21: TODO
Compare Jump-penalization with total variation regulation
Resolve overlapping events
Simulation: not cycle-aligned vs aligned vs full aligned
PWC-only event detection rate
NILM: event detection, device identification, power estimation
Bundle appliances together